## MATERIAL SAFETY DATA SHEET

# SECTION 1 - IDENTIFICATION

PRODUCT NAME:	REIKER ATF TYPE A

EMERGENCY TELEPHONE:  (305) 888 1155

TRADE OWNER: M & J Sunshine, Corporation.                 INFORMATION FAX:  (305) 888 1157

TRADER ADDRESS: 7391 NW 78 Street Miami, FL 33166

SYNONYMS / GENERAL NAME: Automatic Transmission Fluid.

# SECTION 2 – CHEMICAL AND PHYSICAL PROPERTIES

INITIAL BOILING POINT: >280 oC / 536 oF   estimated values	SPECIFIC GRAVITY:  Data Not Available

VAPOUR PRESSURE (mm Hg at 20 oC):  <0.5 	MELTING POINT:  <-40oF (<-49 oC)

VAPOUR DENSITY (air = 1): >1	EVAPORATION RATE:  N/A

SOLUBILITY IN WATER AT 20 oC: Insoluble in cold water	VISCOSITY AT 40oC: 40 mm2/s

STRONG ACID BASE: Stable                                                       PERCENT VOLATILE: Negligible Volatility

APPEARANCE AND ODOR:  Red, light viscous liquid, slight hydrocarbon odor

HAZARDOUS DECOMPOSITION PRODUCTS: On burning, carbon monoxide and carbon dioxide, plus oxides of phosphorus and sulfur.  STABILITY: Stable.    POLYMERIZATION: Not expected to occur.

INCOMPATIBILITY: Strong oxidizers such as hydrogen oxidizer, bromine and chromic acid.

# SECTION 3 – FIRE AND EXPLOSION HAZARD DATA

FLASH POINT:  	176.67oC / 350.01oF

FLAMMABLE LIMITS:   	 Lower: No data     Upper: No data

EXTINGUISHING MEDIA:  Dry chemical , Foam, CO2 or water fog.

SPECIAL FIRE FIGHTING PROCEDURES:  N/A

UNUSUAL FIRE AND EXPLOSION HAZARDS:  Respiratory protection (NIOSH approved) for fire fighting personnel. Cool with water; no unusual products of combustion.

# SECTION 4 – HEALTH HAZARD DATA

PERMISSIBLE CONCENTRATIONS (air): Oil Mist, mineral 5 mg/m3 PEL OSHA, 5 mg/m3 TWA ACGIH

ROUTE(S) OF ENTRY:		Inhalation?  Yes		Skin?  Limited		Ingestion?  Yes (deliberate)

HEALTH HAZARDS-ACUTE TOXICOLOGICAL PROPERTIES:  NDA  Skin:  Prolonged contact may cause dermatitis to some extent.

CARCINOGENICITY:  None     	NTP?  No     IARC Monographs?  No     OSHA Regulated?  No

SIGNS & SYMPTOMS OF EXPOSURE:  Eyes:  Red and drowsy; dizziness, altered personality, nausea, vomiting.

EMERGENCY & FIRST AID PROCEDURES:

Eyes:  Immediately flush with large quantities of water for at least 15 minutes and call a physician if the irritation

persists.

Skin:  Remove excess with cloth or paper. Wash thoroughly with soap and water.

Inhalation:  Remove exposed person to fresh air and ventilate area. Call a physician.

Ingestion:  Call a physician.  Do NOT induce vomiting.  Never give anything by mouth to an unconscious person.

(Continued on Page 2)

ReikerTM - ATF                                                                                                                                                                                Page 2 of 2

# SECTION 5 – CONTROL MEASURES

STEPS TO BE TAKEN IN CASE MATERIAL IS RELEASED OR SPILLED:  In significant volume, transfer into container for disposal. Absorb with inert ingredients such as sand/earth/vermiculite: sweep and dispose according to regulations.`Prevent liquid from entering sewers, watercourses or low areas.  Adequately ventilate area.  Recover free liquid by pumping, or use a suitable absorbent (vermiculite).

WASTE DISPOSAL METHOD:  Dispose of in accordance with all applicable Federal, State and Local regulations.

PRECAUTIONS FOR HANDLING AND STORING:  Keep container closed until ready for use. Keep away from feed

and food products.  Do not handle or store near flame, high heat or strong oxidizers.  Adequate ventilation required.

OTHER PRECAUTIONS:  Do not store or handle in temperatures above 120oF.

# SECTION 6 – PRECAUTIONS FOR SAFE HANDLING AND USE

RESPIRATORY PROTECTIONS:  None.

VENTILATION:	None.

PROTECTIVE GLOVES:  Rubber.

EYE PROTECTION:  Chemical safety goggles.

OTHER PROTECTIVE EQUIPMENT/CLOTHING:  Usually not needed

WORK/HYGIENIC PRACTICES:  Use usual, good hygienic practices; wash thoroughly after use.

# SECTION 7 – TRANSPORTATION DATA

DOT ID No.:  N/A	DOT LABEL REQUIRED:  None

FREIGHT CLASSIFICATION:  Petroleum Lubricating Oil

HAZARD CLASS:  No hazardous	PACKING GROUP:  N/A

SPECIAL TRANSPORTATION NOTED: None.

The information and recommendations contained herein are based upon data believed to be correct.  However, no guarantee or warranty of any kind, expressed or implied, is made with respect to the information contained herein.  This Material Safety Data Sheet was prepared to comply with the OSHA Hazard Communication Standard (29 CFR 1910.1200).  This supersedes any previous information.